## Slide 1: The Plan and Status of NEON
S. Lin for the NEON Collaboration
21st Rencontres du Vietnam, Neutrino Physics - Quy Nhon Nam ward
July 24th, 2025

## Slide 2: Neutrino Telescopes around the World
IceCube (IceCube Gen-2)
South Pole
(P-ONE)
East Pacific Ocean
[KM3Net]
Mediterranean Sea
[Baikal-GVD]
Lake Baikal
(HUNT,TRIDENT,NEON)
South China Sea

## Slide 3: Outline
Simulation and Prospects
Experimental Progress
Summary
Conceptual design
Signal analysis
Sensitivity
PMT Test
OM status
Electronic
Trial

## Slide 4: Outline
Simulation and Prospects
Experimental Progress
Summary
Conceptual design
Signal analysis
Sensitivity
PMT Test
OM status
Electronic
Trial

## Slide 5: Conceptual Design
Neutrino Observatory in the Nanhai (NEON)
Depth: 1700m / 3500m
Detection Volume: ~10 km³
Number of strings: ~1000
Tiling method: Fibonacci spiral
Inter-string distance: ~100m
Inter-OM distance: 40m
31PMT / OM

## Slide 6: Conceptual Design
Neutrino Observatory in the Nanhai (NEON)
Depth: 1700m / 3500m
Detection Volume: ~10 km³
Number of strings: ~1000
Tiling method: Fibonacci spiral
Inter-string distance: ~100m
Inter-OM distance: 40m
31PMT / OM

## Slide 7: Simulation Framework
GENIE for neutrino-nuclear interaction
G4ART: Adopting GPU to simulate tons of cerenkov photons
Digitalization
Track
Cascade
Neutrino interaction

## Slide 8: Noise filtering
The process to filter noise hits from 40K
The 31-PMT OM retains most signals while filtering out noise hits

## Slide 9: Reconstruction
νµ
µ
A GNN-based algorithm has been developed,
with performance similar to the current version
but much faster.

## Slide 10: Reconstruction
A GNN-based algorithm is under development
Cascade event structures are more complex than track events
A reconstruction algorithm developed
  minimize
Median angular error ~ 12 degrees

## Slide 11: Sensitivity
Similar sensitivity to steady sources at 1700 m and 3500 m
Advantage for Galactic center and Centaurus A
A 10-km³ detector achieves 5σ sensitivity of
E2Φ ∼ 3 × 10−10 GeV cm−2 s−1
arXiv:2408.05122

## Slide 12: Outline
Simulation and Prospects
Experimental Progress
Summary
Conceptual design
Signal analysis
Sensitivity
PMT Test
OM status
Electronic
Trial

## Slide 13: PMT Test
Manufacturer | QE(%) | Voltage(V) | Gain | Peak/Valley ratio | Dark Current (nA) | Dark Count (Hz)
North Night Vision | 28.5 | 1005 | 5.34E+06 | 2.05 | 1.35 | 526
Hamamatsu | 27.1 | 1000 | 4.88E+06 | 2.25 | 1.23 | 1178
Valley
Peak
Multi-channel power supply
Multi-channel oscilloscope
Batch Testing
QE~30%
Gain~Nsec_ele
Light

## Slide 14: OM Status
Current Version of OM
8-PMTs / OM
support bracket
Pressure Test:
  works at 4km
Leak Test:
  ~ 0 pressure for 1 day
Tape
Putty
4km ocean depths (40Mpa)
Pressure Test Chamber
Pressure Gauge

## Slide 15: Electronic Design
Front-end and readout electronics

## Slide 16: Electronic Status
Slave
Master
16-Channel Electronic
Channel | σΔt / ns | σTOT / ns | Channel | σΔt / ns | σTOT / ns
shell a ch1 | 0.70 | 0.89 | shell c ch1 | 0.36 | 0.80
shell a ch2 | 0.50 | 0.68 | shell c ch2 | 0.36 | 0.53
shell a ch3 | 0.41 | 0.61 | shell c ch3 | 0.36 | 0.56
shell a ch4 | 0.41 | 0.78 | shell c ch4 | 0.41 | 0.70
shell b ch1 | 0.42 | 0.46 | shell d ch1 | 0.48 | 0.59
shell b ch2 | 0.46 | 0.66 | shell d ch2 | 0.49 | 0.61
shell b ch3 | 0.75 | 0.66 | shell d ch3 | 0.49 | 0.82
shell b ch4 | 0.72 | 0.76 | shell d ch4 | 0.72 | 0.71
Testing Version
Integrated Version
Testing with 10 MHz Signals
For all the channels:
σΔt and σTOT ≤ 1 ns
Packet Loss Rate < 0.001%
Testing with higher signal frequency is on going...

## Slide 17: Trials
buoy
OM 2
OM 1
anchor
26m
2m
Last trial in Qiandao Lake:
Single OM works well under water
Next trial in preparation
→ Validate the time sync system

## Slide 18: Summary
Proposed a deep sea Neutrino Observatory in the Nanhai (NEON)
Built a simulation and analysis framework
Evaluated sensitivity for different sites
Developing optical modules and electronics
Conducted initial underwater trials; next trial in planning
Advancing step by step with ongoing development...

## Slide 19: Thank you for your attention!
21st Rencontres du Vietnam, Neutrino Physics - Quy Nhon Nam ward

## Slide 20: Reconstruction (Appendix)
Vertex
Assuming straight propagation from Vertex to hit position
M-Estimator:
Minimizing T-Res (Melis, 2017)
Cherenkov angle
Shower Vertex Reconstruction of Cascade